## Slide 1
PROJECT PRESENTATION
Disaster Connect
A local-first alert system for floods, earthquakes, storms and tsunamis
It still works when the internet does not.
Python · FastAPI · LangGraph · SQLite · Vanilla JS
Notes: Welcome. This project is a smoke alarm for four natural dangers. It keeps working when the internet does not. Everything in this talk is explained in the report, chapter by chapter.

## Slide 2
When disaster strikes, the network fails first
A smoke alarm needs no Wi-Fi. We built the same idea for four dangers at once.
1
Works offline
The alarm decision never waits for the internet. Weather and shelters are bonuses.
2
Explains itself
Every alert says why, for example “wind 120 km/h is above the limit of 70 km/h”.
3
Easy to run
One zip file and one double-click. Nothing to install.
Notes: A smoke alarm is cheap and works with no Wi-Fi. When a flood or storm hits, phone networks are often the first thing to fail, so we built an alarm that decides locally. Three promises shaped every choice.

## Slide 3
Four dangers, four simple limits
1
Flood
Water level and rain
80 cm
water closer than this, or rain over 30 mm/hr
2
Earthquake
Shaking now vs. usual
3.0×
short-term ÷ long-term average of shaking
3
Storm
Wind, rain, weather code
70 km/h
wind speed, or rain 50 mm/hr, or a thunderstorm code
4
Tsunami
Sea level at the coast
50 cm
rapid change on a tide gauge (not a river)
If several are high, only the most urgent one becomes the headline.
Notes: Each danger has a different fingerprint, so each has its own sensor and its own limit. The water sensor points down at the water, so a smaller distance means higher water. The tsunami detector only trusts a coastal tide gauge, never a river.

## Slide 4
Four layers, one direction of flow
SENSE
Sensors + GPS
Connectivity check
Weather feed
Earthquake catalog
THINK
Flood
Earthquake
Storm
Tsunami
ACT
Combine + explain
Alert dispatcher
SQLite storage
SHOW
FastAPI server
Phone-style web app
Shelter · SOS · Report
Dashed = online extra. Everything else works with no internet.
Notes: Four layers. Sense collects readings, Think turns them into low or high, Act warns people and saves the record, and Show displays it. Dashed boxes are online extras; solid boxes work with no internet.

## Slide 5
One cycle, every five seconds
1
Read
6 sensors + GPS
2
Save
SQLite, synced flag
3
Weather
only if online
4
Detect
4 rule checks
5
Pick worst
priority order
6
Alert
buzzer · SMS · push
7
Sleep
5 s, then repeat
Built to keep going
Every online step has a time limit: connection test 2 s, weather 3 s, language model 4 s. If anything fails, the program carries on with what it has. Worst case is about 14 s per round; offline it is just the 5 s nap.
Notes: One cycle, every five seconds. The program reads, saves, optionally adds weather, runs four detectors, picks the worst result, and only then sends an alert. Every online call has a time limit, so a slow network cannot freeze the loop.

## Slide 6
The detectors are short, readable rules
Detector | Watches | Says HIGH when | Example message
Flood | water distance, rain, forecast rain | water < 80 cm, rain > 30 mm/hr, or forecast > 10 mm | “heavy rain (35.0mm/hr)”
Earthquake | vibration history (last 200 readings) | STA/LTA ratio ≥ 3.0 | “STA/LTA ratio 3.13 exceeds trigger”
Storm | wind, rain, weather code | code 95/96/99, wind ≥ 70, or rain ≥ 50 | “wind speed 120.0 km/h exceeds trigger”
Tsunami | coastal sea-level change | ¦change¦ ≥ 50 cm | “rapid coastal sea-level change 300 cm”
The water sensor measures the distance down to the water, so a smaller number means higher water.
Notes: Each detector is a short Python file with a clear yes or no rule. Because the limits are in one settings file, a person can read them, agree or disagree, and tune them for a new place without touching the logic.

## Slide 7
Earthquake: a spike against calm
Chart: Twenty readings: nineteen quiet, one shock
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Vibration (g) | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.5
STA/LTA
average of the last 5 readings ÷ average of all stored readings. Above 3.0 means HIGH.
New reading | Ratio | Verdict
0.02 g | 1.14 | low
0.30 g | 2.78 | low
0.50 g | 3.13 | HIGH
Same maths as the manual test.
Notes: The ground always trembles a little, so a fixed limit is a poor test. STA over LTA compares the last five readings with the long-run average. Nineteen quiet readings then one at 0.5 g gives a ratio of 3.13, which crosses the 3.0 trigger. A reading of 0.3 g gives 2.78 and stays low.

## Slide 8
One clear headline, decided by rules
1 Tsunami
least time
2 Earthquake
3 Storm
4 Flood
most time
Rules decide
Instant and works offline
Readable: every alert states its reason
No training data needed
The AI only rewords
Optional, online only, 4 s timeout
Turns the reason into one friendly sentence
Can never change the risk level
Notes: When several dangers are high at once, the headline follows how little time people have to react. The most important safety rule in the project is that rules decide and the AI only rewords the sentence; it can never change low to high or high to low.

## Slide 9
Offline first, online as a bonus
ALWAYS WORKS · no internet needed
Read sensors
every few seconds
Check the rules
4 local detectors
Buzzer + SMS
no network needed
BONUS · only when online
Live weather
Open-Meteo, thunderstorm code
Friendly sentence
Groq language model
Push + shelters
OpenStreetMap search
Offline readings are saved as “not synced” and caught up the moment the connection returns.
Notes: The internet is a bonus. The top lane is everything that keeps you safe with no signal. The bottom lane makes alerts richer when a connection exists. Readings taken offline are stored with synced equals zero and caught up when the connection returns.

## Slide 10
Warn people, then remember it
Result is HIGH
Buzzer
local sound
SMS via GSM
no internet
App push
online only
Save alert
SQLite
readings
id · timestamp
lat · lon
water_level_cm
rain_rate_mm_hr
pressure_hpa
vibration_g
wind_speed_kmh
sea_level_change_cm
synced (0 / 1)
alerts
id · timestamp
hazard_type
risk_level
reasoning
lat · lon
mode (online / offline)
Notes: When the result is high, one message goes down several channels. Sound and SMS are guaranteed because they need no internet; app push is a bonus. Every alert is saved in SQLite, a whole database in one file. Today the buzzer and SMS channels print what they would do because no real hardware is connected.

## Slide 11
A phone-style app with five screens
Home
Risk: LOW / HIGH
4 hazard answers
sensors + weather
current risk
Shelter
Nearest place
distance, phone
directions link
nearest safe place
SOS
CALL 112
Police 100
Fire 101
works offline
Prediction
Water chart
Vibration chart
Flood trend
trend charts
Report
Alert 1
Alert 2
Alert 3
alert history
Plain HTML, CSS and JavaScript: nothing to build, works from the zip.
Notes: The app looks like a phone app but runs in any browser. Five screens. The SOS screen needs no internet at all because the phone can place a call by itself. Plain HTML, CSS and JavaScript keep it small and fast.

## Slide 12
Every tool has a reason
Python
readable, runs on a laptop or a Raspberry Pi
FastAPI
fast, checks inputs automatically
LangGraph
runs the detectors as a graph of steps
SQLite
a whole database in one file
STA/LTA
adapts to how noisy a place is
Open-Meteo
free weather, no API key
OpenStreetMap
free shelter and hospital data
Groq
optional friendly sentence only
python-dotenv
keeps secret keys out of the code
GitHub Actions
re-runs the checks on every push
Vanilla JS
no framework, no build step
Embedded Python
zip runs with nothing installed
The full A–Z list is in the report, chapter 12.
Notes: Every tool was picked because it is smaller and simpler than the alternative and keeps working when the internet does not. The complete A to Z list, with what each is and what we chose it instead of, is chapter twelve of the report.

## Slide 13
Send one zip. Double-click. Done.
1
Unzip
anywhere on a Windows PC
2
Double-click START.bat
the bundled Python starts the server
3
Use the app
your browser opens on its own
28 MB
Python + every library inside. Nothing to install and no internet needed to start.
Windows 64-bit
Notes: Most programs fail on someone else's computer because they need software installed first. We bundled a small copy of Python and every library into one folder, so the receiver installs nothing. The private settings file and the developer's database are deliberately left out.

## Slide 14
Tested at five levels
14/14
modules load
7/7
checks passed
5
levels of testing
0
installs needed
What we ran
Full detection cycle, offline
Every web address answered
Wind 120 km/h → storm, sea 300 cm → tsunami
Zip run from a clean folder
Bugs found and fixed
Server still ran old code: restarted
Manual test ignored wind and sea level: fields added
Libraries missing on a fresh Python: bundled
Notes: We tested at five levels, from a quick import check up to running the zip from a clean folder. Everything that can be checked without real hardware passed. Testing also found real problems, which we fixed, such as a server still running old code and a test form that ignored wind and sea level.

## Slide 15
Honest limits, and what comes next
!
Limits today
Sensors are simulated
SMS and buzzer only print to a log
No login on the server
Fixed limits need tuning per place
Not an official warning service
→
Next steps
Real sensors + a SIM800L SMS module
A real upload in the sync step
Push alerts when the app is closed
Several stations agree before alerting
Use the pressure reading for storms
Notes: This is a learning and demonstration project, not an official warning service. The sensors are simulated and SMS is only printed to a log. The next steps are real hardware, a real upload in the sync step, phone push notifications, and having several stations confirm before sounding an alert.

## Slide 16
In short
Simple rules.
Local first.
Every alert explains itself.
Thank you. Questions?
This is a learning project, not an official warning service.
Notes: To close: simple rules, local first, and every alert explains itself. Thank you. Questions are welcome; the full detail is in the 38-page report.